## Slide 1
Introduction to Networking
and the Wireless Edge
AI-Edge summer REU program
Jim Kurose
University of Massachusetts, Amherst

## Slide 2
Overview of today’s REU seminar
Networking 101 - in 20 minutes
Wireless networks: motivation, applications
Architectural components of a wireless network
5G: architectural overview
5G: selected topics for REU
For more information:
Networking: http://gaia.cs.umass.edu/kurose_ross
Wireless Networking: https://gaia.cs.umass.edu/wireless_and_mobile_networking

## Slide 3: The Internet: a “nuts and bolts” view
Internet
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Packet switches: forward packets (chunks of data)
  routers, switches
Communication links
  fiber, copper, radio, satellite
  transmission rate: bandwidth
Billions of connected computing devices:
  running Internet applications
  clients, servers
  5.3 B Internet users (2024)
Networks
  collection of devices, routers, links: managed by an organization

## Slide 4: What is the Internet: a “nuts and bolts” view
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Network edge:
user devices at network edge: clients
servers often in data centers

## Slide 5: Internet-connected devices (not just computers)
Web-enabled toaster +
weather forecaster
Internet phones
Slingbox: remote
control cable TV
Security Camera
IP picture frame
Internet
refrigerator
Tweet-a-watt:
monitor energy use
Amazon Echo
Gaming devices
Pacemaker & Monitor
diapers
cars
scooters
sensor
AR devices
Fitbit
laptop
bikes
wireless and mobile devices

## Slide 6
What is the Internet: a “nuts and bolts” view
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Network core:
  interconnected regional, national, global Internet Service Providers (ISPs): AT&T, Sprint, Level-3, NTT
  interconnected global company networks (e.g., Google, Facebook)
Network edge:
devices, servers connect directly to access networks: (Comcast, Verizon, UMass, company networks)
Network devices:
user devices: aka “clients”
servers often in data centers

## Slide 7: Packet switching
hosts break application-layer messages into packets
network forwards packets from one router to the next, across links on path from source to destination
destination re-assembles packets into application message
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
4 3 2 1

## Slide 8: What’s a protocol?
Human protocols:
“what’s the time?”
“I have a question”
introductions
Network protocols:
computers (devices) rather than humans
all communication activity in Internet governed by protocols
Protocols define the format, order of messages sent and received among network entities, and actions taken on message transmission, receipt
Rules for:
… specific messages sent
… specific actions taken when message received, or other events

## Slide 9: What’s a protocol?
A human protocol and a computer network protocol:
Q: other human protocols?
Hi
Hi
Got the
time?
2:00
time
TCP connection
response
<file>
TCP connection
request
GET http://gaia.cs.umass.edu/kurose_ross
Notes: Explain important points
distributed entities, exchanging messages (governed by protocols)
Time going down
go over definition of protocol (showing format, order of messages sent and received, and actions taken)
We’ll see these kinds of diagrams a lot

## Slide 10: Some foundational questions in networking
Routing: how to choose good paths for packets through the network
Congestion Control: how to control senders so their packets don’t “clog” the network
sender-side of
reliable data transfer protocol
receiver-side
of reliable data transfer protocol
sending process
data
receiving process
data
application
transport
unreliable channel
network
transport
Reliable Data transfer: how to communicate reliably when the channel in-between is unreliable?
Machine learning to the rescue!

## Slide 11: Wireless and Mobile Networks: context
more mobile-broadband-connected (cellular) devices than fixed-broadband-connected devices devices (5-1 in 2025)!
  wireless connectivity even great when WiFi users considered (80% of broadband homes use WiFi)
2007
2008
2009
2010
2011
2012
2013
2014
2015
2016
2017
2018
2019
2020
2021
2022
1000
2000
3000
4000
5000
6000
7000
8000
Mobile broadband subscribers (M)
Fixed (wired) broadband subscribers (M)
Broadband subscribers (M)
Data source: www.statista.com (1/25)
2023

## Slide 12: Wireless and Mobile Networks: context
% global website traffic generated by mobile devices (excluding tablets)
Image source: www.statista.com (11/23)
Majority of Internet web site traffic directed to mobile (rather than fixed) devices

## Slide 13
Wireless applications their needs
Six application areas :
Wide-area Mobile Wireless Internet Access
Local-area Mobile Wireless Internet Access
Fixed Wireless Internet Access
Satellite Networks for Internet Access and Sensing
Cable replacement
Internet of Things (IoT)
user data rate
energy
efficiency
device density
latency
area traffic capacity
mobility
high importance
medium
low
Application needs:
mobility
user data rate
energy efficiency
device density
latency
area traffic capacity

## Slide 14
device ranges over tens or hundreds of miles while maintaining continuous Internet connectivity (e.g., VoIP, streaming, ongoing TCP connection)
only provided by cellular networks
Wide-area Mobile Wireless Internet Access
user data rate
energy
efficiency
device density
latency
area traffic capacity
mobility
high importance
medium
low
wide-area mobile Internet access
Q: two high importance, 1 medium/low importance

## Slide 15
connecting devices (often small, energy-constrained) to computation that senses, monitors, reports, and controls phenomena in the physical world
Bluetooth, WiFi, cellular, LoRaWAN
Internet-of-Things
user data rate
energy
efficiency
device density
latency
area traffic capacity
mobility
high importance
medium
low
Internet of Things
Q: two high importance, 1 medium/low importance

## Slide 16
Overview of today’s REU seminar
Networking 101 - in 10 minutes
Wireless networks: motivation, applications
Elements of a wireless network
5G: architectural overview
5G: selected topics for REU
For more information:
Networking: http://gaia.cs.umass.edu/kurose_ross
Wireless Networking: https://gaia.cs.umass.edu/wireless_and_mobile_networking

## Slide 17: Elements of a wireless network
wired network
infrastructure

## Slide 18: Elements of a wireless network
wired network
infrastructure
wireless hosts
laptop, smartphone, IoT
run applications
may be stationary (non-mobile) or mobile
  wireless does not always mean mobility!

## Slide 19: Elements of a wireless network
wired network
infrastructure
base station
typically connected to wired network
relay - responsible for sending packets between wired network and wireless host(s) in its “area”
  e.g., 4G/5G cell towers, 802.11 (WiFi) access points (APs)

## Slide 20: Elements of a wireless network
wired network
infrastructure
wireless link
typically used to connect device(s) to base station, also used as backbone link
multiple access protocol coordinates link access (random access, FDMA, TDMA, CDMA, polling)
various transmission rates and distances, frequency bands
Ad hoc networks: not all wireless networks are connected into a larger network

## Slide 21: Elements of a wireless network
wired network
infrastructure
wireless device radio
wireless device has different radios for different networks
iPhone16: has ~11 different radios, many antennae
  5 different cellular radios, WiFi, Bluetooth, UWB, satellite NFC, GPS
Notes: 5G NR (New Radio): Supports both Non-Standalone (NSA) and Standalone (SA) modes, encompassing sub-6 GHz and mmWave frequencies for high-speed data transmission.
LTE (Long-Term Evolution): Includes support for both Frequency Division Duplexing (FDD) and Time Division Duplexing (TDD) variants, facilitating widespread 4G connectivity.
WCDMA (Wideband Code Division Multiple Access): Provides compatibility with 3G networks, ensuring service continuity in areas where newer technologies are unavailable.
HSPA+ (Evolved High-Speed Packet Access): Enhances 3G network performance, offering faster data rates and improved efficiency.
GSM (Global System for Mobile Communications): Ensures basic voice and data services, particularly in regions where GSM remains prevalent.

## Slide 22: Wireless networks: radio
Wireless radio
signal carried in various “bands” in electromagnetic spectrum
no physical “wire”
broadcast, “half-duplex” (sender to receiver)
propagation environment effects
  reflection
  obstruction by objects
  interference/noise
Radio link types:
Wireless LAN (WiFi)
  10-1000’s Mbps; 10’-100s of meters
wide-area (e.g., 4G/5G cellular)
  10’s Mbps over ~10 Km
  Gbps over short distances (mmwave)
Bluetooth: cable replacement
  short distances, limited rates
satellite
  geostationary: < 45 Mbps per channel, 270 msec e-e delay
  LEOS: 50-100 Mbps downlink (Starlink), 46 msec LEOS
Notes: Recent Starlink speeds: https://arstechnica.com/tech-policy/2022/09/ookla-starlinks-median-us-download-speed-fell-nearly-30mbps-in-q2-2022/

## Slide 23: Characteristics of selected wireless links
Indoor
Outdoor
Midrange
outdoor
Long range
outdoor
10-30m
50-200m
200m-4Km
4Km-15Km
2 Mbps
4G LTE, 5G eMBB
802.11ac
802.11n
802.11g
802.11b
3.5 Gbps
600 Mbps
54 Mbps
11 Mbps
Bluetooth
802.11ax
14 Gbps
5G
10 Gbps
802.11 af,ah
Space (100’s of Km)
LEOS

## Slide 24: 802.11 (WiFi) LAN architecture (overview)
wireless host communicates with base station
Basic Service Set (BSS) (aka “cell”) in infrastructure mode contains:
  wireless hosts
  wireless channel
  access point (AP): base station
other network services (identity management, IP addressing and routing, DHCP) handled by institutional IP infrastructure: WiFi is a layer-2 (only) network!
BSS 1
BSS 2
institutional
network,
Internet
switch
or router

## Slide 25
Overview of today’s REU seminar
Networking 101 - in 10 minutes
Wireless networks: motivation, applications
Architectural components of a wireless network
5G: architectural overview
5G: selected topics for REU
For more information:
Networking: http://gaia.cs.umass.edu/kurose_ross
Wireless Networking: https://gaia.cs.umass.edu/wireless_and_mobile_networking

## Slide 26
Architectural Elements of 5G
radio access
Network (RAN)
to
Internet
5G core network
gNodeB
User equipment
(UEs)
Core Network Functions

## Slide 27: Wireless networks: edge and core networks
…
Mobile device
(UE)
Base station
(eNode-B)
…
Mobile device
(UE)
Base station
(gNode-B)
Mobility Management Entity (MME)
Internet
Institutional wired network
=
WLAN 1
WLAN 2
Internet
edge
core
edge
core
WiFi:
5G:
UMass 7K Wi-Wi APs
Notes: VIDEO
Let’s wrap up our discussion of elements of a wireless network with the big picture about the structure of wireless networks.
Here, probably the most important characterization to keep in mind - the edge/core distinction. This is particularly true when we’re studying WiFi and Cellular networks.
Audio:
Let’s start with WiF over here on the lefti. The edge network in a WiFi setting is the wireless network itself. In an institutional setting (e.g., your university or company), the WiFi network connects into the wired infrastructure of the institution, just as an Ethernet local area network would do. In this case, WiFi is really just a link-layer wireless technology, just like Ethernet. Traffic flows from through the WiFi Wireless LAN through the intuitional network, and through the Internet.
In the cellular setting, the edge network is known as the radio access network (RAN). It’s got the iconic cell tower and base station, devices, and radio channels we discussed above. But a cellular network operator runs more than just radio access network. It also runs a core network, where support for mobility in the wide area, identity management, and many additional services are implemented. Traffic flows from through the radio access networking through the data plane of the core network, and through the Internet.
The Core network is a really unique and interesting feature of cellular networks, and something we’ll study in depth later. So just keep this idea of a core network parked in the back of your mind for now.
And with that, we’ve wrapped up our high-level discussion of architectural components of a wireless network.

## Slide 28
5G Radio Access Network (RAN)
gNodeB
User equipment
(UEs)
5G RAN: edge network connecting devices (UEs) to base station (gNodeB)
provides link-layer service, as first hop between devices and larger network
limited geographic scope
under control of a single service provider
somewhat analogous to WiFi LAN
RAN components:
  many devices (User Equipment: UE)
  radio channel (New Radio: NR)
  one base station (Next Generation Node B: gNodeB, gNB)

## Slide 29
5G RAN components
gNodeB
User equipment
(UEs)
5G User Equipment (UE):
smartphone, tablet, laptop, IoT device
UEs host, run applications
devices attached in RAN
may or may not be mobile

## Slide 30
5G RAN components
gNodeB
User equipment
(UEs)
Radio Channel (aka New Radio, NR, in 5G)
Physical (PHY) layer: OFDMA
UEs only communicate with base station
  via uplink, downlink channels
  UEs do not communicate directly with each other
various uplink/downlink physical and logical channel defined

## Slide 31
5G RAN components
gNodeB
User equipment
(UEs)
Base station (aka Next Generation Node B (gNodeB or gNB in 5G):
central control point for RAN, role somewhat analogous to that of WiFi AP
computing, storage may be located at gNB
all communication between UEs and other endpoints (other UEs, 5G Core, Internet) go through gNB
aka Extended Node B (eNB) in 4G

## Slide 32
5G Core Network
to
Internet
Core Network Functions
Core situated between RAN and other endpoints (Core, larger Internet)
  single Core; multiple RANs
consist of links, routers, servers, providing services to UEs and gNBs
  “all Internet” Core, but very different services than traditional Internet apps
clear logical separation between control-plane, user plane:
  CUPS: Control-Plane and User-Plane Separation

## Slide 33: 5G control- and user- plane separation (CUPS)
control plane
functionality for managing and configuring network devices (routing, wireless resource allocation)
user mobility management, security, authentication
gNB, RAN
base station
(gNB)
S-GW
user plane
5-layer Internet data plane
extensive use of tunneling
IP tunnel
AMF
Access, Mobility
Management
SMF
Session
Management
PCF
Policy control
AUSF
Authentication
Server
UDM
Unified Data Management
AF
Application Function
IP datagrams
Notes: Video:
So software-ization and the ability to execute user-created applications locally are two big differences between 4G and 5G.
Let’s wrap up our discussion of 4G and 5G networks noting a common worldview taken in both 4G and 5G networks.
That is, the distinction between the control-plane and the user-plane in a 4G or 5G network
This is something that you may have learned about already in an introductory networking course that emphasized wired networks. The concept is equally important in wireless networks.
Audio:
The control plane is comprised of the components and functionality for managing and configuring network devices for routing, and for wireless resource allocation. Components and functionality for managing user mobility and user authentication are also part of the control plane. So, for example, the MME and HSS in 4G and the sort-of-equivalent AMF and SMF functions in 5G are definitely control-plane components.
The user plane is comprised of the network components and protocols that carry user packets to/from end user devices and their ultimate sources or destinations. So the data paths in the network’s routers, gNB’s and user devices are part of the user plane. The packet queues within these devices, link-layer channel access and transmission protocols, and the tunnels that carry user packets between devices are also part of the user plane. We’ll see extensive use of tunneling in 4G and 5G data planes. These tunnels are also part of the data plane.
Indeed, the logical separation of control and user planes is so foundational in 4G and 5G architectures that (of course!) it even has its own name and acronym in the standards: CUPS, which stands for Control Plane and User Plane Separation!

## Slide 34: RAN packet processing pipeline: context
Base station
(gNode-B)
IP datagrams
RAN: transfers datagrams between mobile core and UEs
UE
datagrams
protocol processing pipeline in UE

## Slide 35: RAN packet processing pipeline
RRC
PDCP
RLC
MAC
D/A
conversion
RF
front end
PHY
base station
control
plane
user
plane
mobile
core
traditional 3GPP view
datagrams
RRC (Radio Resource Control)
configures coarse-grained, policy-related aspects of pipeline (e.g., scheduling prioritization, security)
this implements the RAN’s control plane
does not process user plane packets

## Slide 36: Software-defined RAN
Recall our earlier description of traditional RAN base station (below)
tightly coupled control and data planes
let’s focus on control / management: RRC implementation

## Slide 37: Software-defined RAN
  SD-RAN: implementing RAN using SDN approach
Control plane proxy
PDCP
RLC
MAC
D/A
conversion
RF
front end
PHY
control
plane
user
plane
Real-Time Intelligent Controller (RIC)
3GPP-compliant interface between RAN and Mobile Core control plane
New programmatic API for exerting software-based control over pipeline that implements RAN user plane
Re-factored RRC
SDN-controlled switches

## Slide 38: Software-defined RAN
  SD-RAN: implementing RAN using SDN approach
Control plane proxy
PDCP
RLC
MAC
D/A
conversion
RF
front end
PHY
control
plane
user
plane
Real-Time Intelligent Controller (RIC)
Re-factored RRC
SDN-controlled switches
RAN Network Information Base (R-NIB)
common set of information consumed by numerous control apps, e.g., longer time-scale CQI (channel Quality Indicator) values, other per-session state
R-NIB
load
balancing
handover
QoS
Near-real time network control applications implemented as “xApps”
…
…

## Slide 39: Mobility in 5G networks: major mobility tasks
Visited network
Streaming server
Home
network
Internet
1
3
4
association:
covered earlier
mobile provides IMSI – identifying itself, home network
1
control-plane configuration:
AMF, visited UDM, home UDM establish control-plane state: mobile in visited network
2
data-plane configuration:
AMF, SMF configures forwarding tunnels
visited, home network establish tunnels from home to mobile, only if home-routed
3
mobile handover:
mobile device changes its point of attachment to visited network
4
AMF
AUSF
SMF
PCF
UDM
SEPP
1
AMF
AUSF
SMF
PCF
UDM
SEPP
2

## Slide 40
Summary of today’s REU seminar
Networking 101 - in 20 minutes
Wireless networks: motivation, applications
Architectural components of a wireless network
5G: architectural overview
5G: selected topics for REU
For more information:
Networking: http://gaia.cs.umass.edu/kurose_ross
Wireless Networking: https://gaia.cs.umass.edu/wireless_and_mobile_networking
Enjoy this summer REU!